## Slide 1
RISC&CISC

## Slide 2
RISC&CISC
Reasons for increased complexity
1.Microcode and LSI Technology
2.Code Density
3.Marketing Strategy
4.Upward Compatibility
5.Support for High Level Languages
6.Use of Multiprogramming

## Slide 3
RISC&CISC
Compexity
Patterson:
We shall argue that in many cases the complex instruction sets are more detrimental than useful. The trend of architecture is toward more complex machines, but the trend is not always cost-effective.
Clark:
“Reduced” and “Complex” is a false dichotomy. The paper contains no formal definition of a RISC or a CISC. “In many cases the complex instruction sets are more detrimental than useful” is meaningless.

## Slide 4
RISC&CISC
Code density
Patterson:
Code compaction can be as easily achieved merely by cleaning up the original instruction set. While code compaction is important, the cost of 10% more memory is often far cheaper than the cost of squeezing 10% out of the CPU by architectural "innovations."
Clark:
Their case for the RISC boils down to the sentence “We suspect that code compaction can be as easily achieved by cleaning up the original instruction set”, which is not convincing without supporting evidence.

## Slide 5
RISC&CISC
code density
Patterson:
Code compaction can be as easily achieved merely by cleaning up the original instruction set. While code compaction is important, the cost of 10% more memory is often far cheaper than the cost of squeezing 10% out of the CPU by architectural "innovations."
Clark:
Their case for the RISC boils down to the sentence “We suspect that code compaction can be as easily achieved by cleaning up the original instruction set”, which is not convincing without supporting evidence.

## Slide 6
RISC&CISC
Support for High Level Languages
Patterson:
In many cases the complex instruction sets are more detrimental than useful. Very few opcodes account for most of a program’s execution.
Clark:
For different languages, the needs for the complexity of instructions are different.

## Slide 7
RISC&CISC
Design Time
Patterson:
It s clear that reduced design time would have very positive benefits on the resulting machine. Design difficulty is a crucial factor in the success of VLSL computer.
Clark:
There are numerous time-consuming process in a large company designing products for high-volume manufacturing that do not exist in a small company designing products for low-volume manufacturing

## Slide 8
RISC&CISC
Ease of Compiler-Writing
Patterson:
Compilers are often unable to utilize complex instructions, nor do they use the insidious tricks in which assembly language programmers delight. Only a fairly small part of the architecture is being used.
Clark:
The complex code generation can be build by simple ones. So the cost is not high.

## Slide 9
RISC&CISC
Design Errors
Patterson:
One of the major problems of complex instruction sets is debugging the design.
Clark:
In a RISC, the compiler and run-time system would bear the burden formerly norne by microcode, and implementation errors would presumably turn up in this software.