## Slide 1: Advanced Computer Architecture (ACA2020)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2020

## Slide 2: Lecture 05 Advanced Branch Predictions and Tomasulo's Algorithm
November 17, 2020

## Slide 3: Computers in the News – From David Patterson cs252-s06
C. Al Gore, 2000
"Again, I'd repeat to you that if we can remain the most competitive nation in the world, it will benefit the worker here in America. People have got to understand, when we talk about spending your taxpayers' money on research and development, there is a correlating benefit, particularly to your children. See, it takes a while for some of the investments that are being made with government dollars to come to market. I don't know if people realize this, but the Internet began as the Defense Department project to improve military communications. In other words, we were trying to figure out how to better communicate, here was research money spent, and as a result of this sound investment, the Internet came to be.
The Internet has changed us. It's changed the whole world."

## Slide 4: A Bad Graduate Career: David Patterson
Concentrate on getting good grades:
  Postpone research involvement: might lower GPA(?)
Minimize number and flavors of courses
  Why take advantage of 1 of the top departments with an emphasis on excellent grad courses?
  Why take advantage of a campus with 35/36 courses in the top 10?
  May affect GPA

## Slide 5: How to Have a Bad Graduate Career
Don’t trust your advisor
  Advisor is only interested in his or her own career, not your’s
  Advisor may try to mentor you, use up time, interfering with GPA
Only work the number of hours per week you are paid!
  Don’t let master class exploit the workers!
Work at home as much as possible
  Avoid distractions of talking to others

## Slide 6: Concentrate on Graduating as Fast as Possible
Winner is first in class to PhD!
People only care about that you have a PhD and your GPA, not on what you know
  Nirvana: graduating in 3.5 years with a 4.0 GPA!
Don’t spend a summer in industry: takes longer
  How could industry experience help with selecting PhD topic?

## Slide 7: Concentrate on Graduating as Fast as Possible
Don’t work on large projects: takes longer
  Have to talk to others, have to learn different areas
  Synchronization overhead of multiple people
  You’ll get lost
Don’t do a systems PhD: takes longer
Don’t waste time polishing writing or talks
  Again, that takes time

## Slide 8: Concentrate on Graduating as Fast as Possible
Don’t go to conferences
  It costs money and takes time; you’ll have plenty of time to learn the field after graduating
  ( This may not be true in our situation )
    You may take the conference opportunities to travel/tour around, especially during the vacation

## Slide 9: Next …
Correlating Branch Predictors (m, n)

## Slide 10: A One Bit Correlation Predictor (1, 1)
A two bits predictor
  One bit for the last branch not taken
  The other for the last branch taken
In general, the last branch executed is not the same instruction as the branch being predicted
  Although this can occur in simple loops consisting of a single basic block
A two BPSs predictor

## Slide 11: Implementation of a 1-bit Correlation Predictor (1, 1) and (0, 2)
(1,1) | (1-bit) |  | (1-bit)
Lower bits of a branch address |  |  | 
 | NT | Last branch selector (1-bit) | T
(0,2) | (1-bit) | (1-bit)
Lower bits of a branch address |  | 
How can two BPBs
work together?
The same memory capacities

## Slide 12: Two-Level Branch Predictor (2, 2)
Pentium Pro uses the result from the last two branches to select one of the four sets of BHT(BPB) bits (~95% correct)
0
0
k
Fetch PC
Shift in Taken/¬Taken results of each branch
2-bit global branch history shift register
Taken/¬Taken?

## Slide 13: Correlating Branches: Another View
(2,2) predictor
Behavior of recent branches selects between four predictions of next branch, updating just that prediction
Branch address
2-bits per branch predictor
Prediction
2-bit global branch history
4

## Slide 14: Comparison of 2-bit Predictors: Mis
Chart: 
| li | eqntott | gcc | fpppp | spice | doduc | tomcatv | matrix300 | nASA7
4096 entries: 2 bits per entry | 0.1 | 0.18 | 0.05 | 0.09 | 0.09 | 0.05 | 0.01 | 0 | 0.01
Unlimited entries: 2 bits per entry | 0.1 | 0.18 | 0.05 | 0.09 | 0.09 | 0.05 | 0 | 0 | 0
1024 entries: (2,2) | 0.05 | 0.06 | 0.04 | 0.05 | 0.05 | 0.05 | 0.01 | 0 | 0.01

## Slide 15: Tournament Predictors
Multilevel branch predictor
  Adaptively combining local and global predictors
Use n-bit saturating counter to choose between predictors
  Usual choice between global and local predictors

## Slide 16: Branch Predictions
Basic 2-bit predictor:
  For each branch, predict taken or not taken
  If the prediction is wrong two consecutive times, change prediction
Correlating predictor:
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes of preceding n branches
Local predictor:
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes for the last n occurrences of this branch
Tournament predictor:
  Combine correlating predictor with local predictor

## Slide 17: Branch predictor performance

## Slide 18: The Intel Core i7 Branch Predictor
Intel has released only limited amounts of information about the Core i7’s branch predictor, which is based on earlier predictors used in the Core Duo chip
Each predictor combines three different predictors
  (1) the simple two-bit predictor
  (2) a global history predictor
  (3) a loop exit predictor
    The loop exit predictor uses a counter to predict the exact number of taken branches (which is the number of loop iterations) for a branch that is detected as a loop branch

## Slide 19: The Misprediction Rate for 19 of the SPECCPU2006

## Slide 20: Next …
Overcoming Data Hazards with Dynamic Scheduling

## Slide 21: Dynamic Scheduling Advantages and …
Hardware rearrange order of instructions to reduce stalls while maintaining data flow
Advantages:
  Compiler doesn’t need to have knowledge of microarchitecture
  Handles cases where dependencies are unknown at compile time
  It allows code that compiled for one pipeline to run efficiently on a different pipeline
Disadvantage:
  Substantial increase in hardware complexity
  Complicates exceptions

## Slide 22: Dynamic Scheduling Needs …
Dynamic scheduling implies
  Out-of-order execution
  Out-of-order completion
Dynamic execution creates the possibility for WAR and WAW hazards
  Hardware register renaming
Tomasulo’s Approach: IBM 360/91
  Tracks when operands are available
  Introduces register renaming in hardware
    Minimizes WAW and WAR hazards

## Slide 23: The Front Panel of System 360 Model 91

## Slide 24: Another Dynamic Algorithm: Tomasulo’s Algorithm
Differences between IBM 360 & CDC 6600 ISA
  IBM has only 2 register vs. 3 in CDC 6600
  IBM has 4 FP registers vs. 8 in CDC 6600
  IBM has memory-register ops
Why Study?
  Lead to Alpha 21264, HP 8000, MIPS 10000, Pentium II, PowerPC 604, …

## Slide 25: Tomasulo Organization
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6

## Slide 26: Three Stages of Instruction Goes
The ID and EX stages of the five-stage pipeline are replaced with three new stages
  Issue
  Execute
  Write result

## Slide 27: Tomasulo Algorithm 1/2
Control & buffers distributed with FU
  FU buffers called reservation stations (RS) have pending operands
Load Buffer and Stores Buffer treated as FUs with RSs as well
Registers replaced by values or pointers to RS called register renaming
  Renaming avoids WAR, WAW hazards
  More reservation stations than registers, so can do optimizations compilers can’t

## Slide 28: Tomasulo Algorithm 2/2
Results to FU from RS, not through registers, but over Common Data Bus (CDB) that broadcasts results to all FUs
  Avoids RAW hazards by executing an instruction only when its operands are available
Integer instructions can go past branches (predict taken), allowing FP ops beyond basic block in FP queue

## Slide 29: Fields of Reservation Stations
Op: The operation to perform
Vj, Vk: value of the source operands
  Only one of V or Q is valid for each operand
Qj, Qk: RSs producing source registers
  Qj, Qk = 0 => ready
Busy: indicates this reservation station and its accompanying FUs are occupied

## Slide 30: Register File Has a Field
Qi: the reservation station that contains the operation whose result should be stored into this register
  If the value of Qi is blank (0), no currently active instruction is computing a result for this register (where is the value?)

## Slide 31: Load And Store Buffers
Each have a filed A
  A: hold the effective address
The store buffer also has a V field
  V: value of the operands

## Slide 32: How It Works: Previous Example
L.D F6, 34(R2)
L.D F2, 45(R3)
MUL.D F0, F2, F4
SUB.D F8, F2, F6
DIV.D F10, F0, F6
ADD.D F6, F8, F2

## Slide 33: Tomasulo Example
Clock cycle counter
FU count
down
Instruction stream
3 Load/Buffers
3 FP Adder R.S.
2 FP Mult R.S.

## Slide 34: Tomasulo Example Cycle 1

## Slide 35: Tomasulo Example Cycle 2
Note: Can have multiple loads outstanding

## Slide 36: Tomasulo Example Cycle 3
Note: MULT issued, registers are removed (“renamed”) in RSs
Load1 exec completing; what is waiting for Load1?

## Slide 37: Tomasulo Example Cycle 4
Load2 exec completing

## Slide 38: Tomasulo Example Cycle 5
Timer starts down for Add1, Mult1

## Slide 39: Tomasulo Example Cycle 6
Issue ADDD here despite name dependency on F6?

## Slide 40: Tomasulo Example Cycle 7
Add1 (SUBD) completing; what is waiting for it?

## Slide 41: Tomasulo Example Cycle 8

## Slide 42: Tomasulo Example Cycle 9

## Slide 43: Tomasulo Example Cycle 10
Add2 (ADDD) completing; what is waiting for it?

## Slide 44: Tomasulo Example Cycle 11
Write result of ADDD here?
All quick instructions complete in this cycle!

## Slide 45: Tomasulo Example Cycle 12

## Slide 46: Tomasulo Example Cycle 13

## Slide 47: Tomasulo Example Cycle 14

## Slide 48: Tomasulo Example Cycle 15
Mult1 (MULTD) completing; what is waiting for it?

## Slide 49: Tomasulo Example Cycle 16
Just waiting for Mult2 (DIVD) to complete

## Slide 50: Tomasulo Example Cycle 16-54
Faster than light computation (skip a couple of cycles)

## Slide 51: Tomasulo Example Cycle 55

## Slide 52: Tomasulo Example Cycle 56
Mult2 (DIVD) is completing; what is waiting for it?

## Slide 53: Tomasulo Example Cycle 57
Once again: In-order issue, out-of-order execution and out-of-order completion.
57

## Slide 54: The Code
LOOP: L.D F0,0(R1)
MUL.D F4,F0,F2
S.D 0(R1),F4
DADDUI R1,R1,#-8
BNE R1,R2,LOOP

## Slide 55: Predict
All branches are taken!
The reservation stations will allow multiple executions of the loop
  The loop is unrolled dynamically by the hardware

## Slide 56: Snapshot Time Assume
All of the instructions in two successive iterations of the loop have issued
  But none has completed
The load and store buffers contain the addresses to be loaded from and stored to
The load values are in the load buffers
The store buffers indicate that the multiply destinations are the values to store

## Slide 57: Instruction Status

## Slide 58: Status of FUs and Registers

## Slide 59: Instruction Status
The distribution of the hazard detection logic
  Distributed reservation stations and the CDB
  The waited operands can be released simultaneously by broadcast on CDB
The elimination of WAW and WAR hazards

## Slide 60: WAR Hazard Involving F6
If the first L.D which provides the value of F6 for DIV.D has completed, then Vk will store the result allowing DIV.D to execute independent of ADD.D
If L.D has not completed, then Qk would point to the first L.D and DIV.D would still be independent of ADD.D

## Slide 61: 4-bit Tag Fields of RS
In our example, the tag field is a 4-bit quantity that denotes
  4 registers
  5 reservation stations
  6 load buffers
Value 0000b indicate that the operand is already available in the registers

## Slide 62: Notes
A table of instruction status is used to illustrate the algorithm, but it is NOT part of the hardware
The entries in the table are distributed throughout the hardware

## Slide 63: Tomasulo Drawbacks
Complexity
Performance limited by CDB
  CDB must go to multiple functional units  high capacitance, high wiring density
  Number of functional units that can complete per cycle limited to one!
    Multiple CDBs  more FU logic for parallel assoc stores
Non-precise interrupts!
  We will address this later

## Slide 64: Issue FP Operation
Station r empty
Bookkeeping
  if (RegisterStat[rs].Qi  0) //Vj
  RS[r].Qj  RegisterStat[rs].Qi
  else RS[r].Vj  Regs[rs]; RS[r].Qj  0;
  if (RegisterStat[rt].Qi  0) //Vk
  RS[r].Qk  RegisterStat[rt].Qi
  else RS[r].Vk  Regs[rs]; RS[r].Qk  0;
  RS[r].busy  yes; RegisterStat[rd]. Qi  r；
  RS[r].Op  OP;

## Slide 65: Issue Load or Store 1/2
Buffer r empty
Common bookkeeping
  if (RegisterStat[rs].Qi  0)
  Buffer[r].Qj  RegisterStat[rs].Qi
  else RS[r].Vj  Regs[rs]; Buffer[r].Qj  0;
  Buffer[r]. A  imm；Buffer[r].busy  yes；
  Buffer[r].Op  OP；

## Slide 66: Issue Load or Store 2/2
Load only:
  RegisterStat[rt].Qi  r
Store only:
  if (RegisterStat[rt].Qi  0)
  RS[r].Qk  RegisterStat[rs].Qi
  else
  RS[r].Vk  Regs[rt];
  RS[r].Qk  0;

## Slide 67: Execution of FP operation
Wait until (RS[r].Qj=0) and (RS[r].Qk=0)
Action or bookkeeping
  None-operands are in Vj and Vk

## Slide 68: Execution Load-Store Step 1
(RS[r].Qj=0) and r is head of load-store queue (buffer)
Action or bookkeeping:
  RS[r].A ← RS[r].Vj + RS[r].A;

## Slide 69: Execution Load-Store: Load Step
Load-store step 1 complete
Action or bookkeeping:
  Read from Mem[RS[r].A]

## Slide 70: Write Result: FP Operation or Load
Execution complete at r & CDB available
Bookkeeping
  ∀x(if (RegisterStat[x].Qi=r) {Regs[x] ← result; RegisterStat[x].Qi←0} );
  ∀x(if (RS[x].Qj=r) {RS[x].Vj ← result; RS[x].Qj ← 0});
  ∀x(if (RS[x].Qk=r) {RS[x].Vk ← result;RS[x].Qk ← 0});
  RS[r].Busy ← no;

## Slide 71: Write Result: Store
Wait until execution complete at r & RS[r].Qk=0
Action or bookkeeping
  Mem[RS[r].A]←RS[r].Vk;
  RS[r].Busy← no;

## Slide 72: Loop and Unrolling
To fully understand how Tomasulo's algorithm eliminates WAW and WAR hazards, we need to look at a loop
Consider an example similar to the one we used to demonstrate loop unrolling where the elements of an array are multiplied by a scalar in F2

## Slide 73: Bob Tomasulo Created An Approach
The reservation stations extent the real register set via the renaming process
  The 360 architecture: only 4 FP registers
Supports overlapped execution of multiple copies of the same loop with only a small number of registers used by the program

## Slide 74: The Code
LOOP: L.D F0,0(R1)
MUL.D F4,F0,F2
S.D 0(R1),F4
DADDUI R1,R1,#-8
BNE R1,R2,LOOP

## Slide 75: Predict
All branches are taken!
The reservation stations will allow multiple executions of the loop
  The loop is unrolled dynamically by the hardware

## Slide 76: Snapshot Time Assume
All of the instructions in two successive iterations of the loop have issued
  But none has completed
The load and store buffers contain the addresses to be loaded from and stored to
The load values are in the load buffers
The store buffers indicate that the multiply destinations are the values to store

## Slide 77: Instruction Status

## Slide 78: Status of FUs and Registers

## Slide 79: What Can We Found?
CPI close to 1
The load instruction from the second iteration could easily complete before the store from the first iteration
The load and store can safely be done in a different order, provided they access different addresses
  The load is before the store
    Interchanging them results in a WAR hazard
  The store is before the load
    Interchanging them results in a RAW hazard

## Slide 80: Load
Completed effective address calculation
Check an address conflict by examining the A field of all active store buffers
  If load address = any active store address
  The load instruction is not sent to the load buffer
  Until the conflicting store completes
    (?)

## Slide 81: Stores
Similarly
Except must check for conflicts in both the load buffers and the store buffers
Since conflicting stores cannot be reordered with respect to either a load (WAR) or a store (WAW)
Meny research you may do in memory access to optimize the ...

## Slide 82: Usage of Tomasulo’s Scheme
The designer is forced to pipeline an architecture obtain high performance without pipeline specific compiler
Difficult to schedule code
A shortage of registers

## Slide 83: Key Components in Tomasulo’s
Dynamic scheduling with RSs
  Permit instruction issue past branches
  Buffer old values of registers - avoiding WAR
Register renaming
  Multiple iterations use different physical destinations for registers
Dynamic memory disambiguation
Other perspective: Tomasulo building data flow dependency graph on the fly

## Slide 84: Homework
Book reading
  3.3~3.5
Paper reading
  "An Efficient Algorithm for Exploiting Multiple Arithmetic units", Tomasulo, IBM Journal, January 1967
Coding
  Tomasulo’ algorithm with the following loop test
    LOOP: L.D F0,0(R1)
    MUL.D F4,F0,F2
    S.D 0(R1),F4
    DADDUI R1,R1,#-8
    BNE R1,R2,LOOP

## Slide 85: Next…
Speculation