## Slide 1: Advanced Computer Architecture (ACA2020)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2020

## Slide 2: Lecture 07 Hardware-Based Speculation
November 25, 2020

## Slide 3: HW Speculation and Prediction
HW speculation is subtle, but important, extension over branch prediction with dynamic scheduling
HW speculation
  Fetch, issue, and execute instructions, as if predictions are always correct
  Dynamic scheduling only fetches and issues such instructions

## Slide 4: What about Precise Exceptions/Interrupts?
Recall: an interrupt or exception is precise if there is a single instruction for which:
  All instructions before that have committed (finished) their state
  No following instructions (including the interrupting instruction) have modified any state
Both Scoreboard and Tomasulo have
  In-order issue
  out-of-order execution
  out-of-order completion --> we need order

## Slide 5: Tomasulo's Structure
Instructutions to RSs
RSs to FUs
FUs to CDB
CDB to all
Problem: out-of-order complation
----> keep order!
Instruction Fetch
Issue
Register File
FU

## Slide 6: On issue
Reserve slot at tail of ROB
Record dest reg, PC
Tag u-op with ROB slot
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 7: Done execute
Deposit result in ROB slot
Mark exception state
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 8: WB head of ROB
Check exception, handle
Write register value, or
Commit the store
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 9: Reorder Buffer + Forwarding
Forwarding committing results to later uncommitted operations
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 10: Reorder Buffer + Forwarding + Speculation
Issue branch into ROB
Mark with prediction
Fetch and issue predicted instructions speculatively
Branch must resolve before leaving ROB
Resolve correct
  Commit following instr
Resolve incorrect
  Mark following instr in ROB as invalid
  Let them clear
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 11: What is that like?
Tomasulo's!
The key ideas
  Out-of-order execution
  Force them to in order commit
    Prevent any irrevocable action, such as an exception, until an instruction commits
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 12: 3 components of HW-based speculation
Dynamic branch PREDICTION to choose which instructions to execute
Dynamic SCHEDULING different combinations of basic blocks
Speculation allow EXECUTION of instructions before control dependences are resolved
  Ability to UNDO incorrectly speculated

## Slide 13: Several Modern Processors
PowerPC
MIPS
Intel
Alpha
AMD

## Slide 14: Where to Commit: Reorder Buffer (ROB)
Hold the results of instructions that have finished execution BUT have not committed
Pass results among instructions that may be speculated
Provides additional registers as the reservation stations in Tomasulo’s algorithm

## Slide 15: Reorder Buffer (ROB)
Reorder
Buffer
FP
Op
Queue
FP Adder
FP Adder
Res Stations
Res Stations
FP Regs
Commit path

## Slide 16: Fields of ROB
1. Instruction type (op code): indicates instructions
  A branch (and has no destination result)
  A store (which has a memory address destination)
  A register operation (ALU operation or load, which have register destinations)
2. Destination field: where the instruction result should be written
  The register number (for loads and ALU operations)
  The memory address (for stores)
3. Value: hold the value of the instruction result until the instruction commits
4. Ready: indicates that instruction has completed execution, and the value is ready

## Slide 17: MIPS with ROB Using Tomasulo’s
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 18: Stages of Tomasulo’s Speculation
Issue
Execute
Write result
Commit
  Additional stage

## Slide 19: Speculation: Example
To illustrate how the new Tomasulo’s algorithm works
  L.D F6,34(R2)
  L.D F2,45(R3)
  MUL.D F0,F2,F4
  SUB.D F8,F6,F2
  DIV.D F10,F0,F6
  ADD.D F6,F8,F2

## Slide 20: Speculation: Assumptions
Assume again
  Add is 2 clock cycles
  Multiply is 10 cycles
  Divide is 40 cycles
Show the status table of the code section execution
  (When the MUL.D is ready to go to commit - in the textbook)

## Slide 21: Speculation: Original
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
L.D F6,34(R2)
L.D F2,45(R3)
MUL.D F0,F2,F4
SUB.D F8,F6,F2
DIV.D F10,F0,F6
ADD.D F6,F8,F2

## Slide 22: Speculation: Clock 1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
L.D F6,34(R2)
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
1 34+R2
Dest
Reorder Buffer
Registers
L.D F6,34(R2)
L.D F2,45(R3)
MUL.D F0,F2,F4
SUB.D F8,F6,F2
DIV.D F10,F0,F6
ADD.D F6,F8,F2

## Slide 23: Speculation: Clock 2
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F6
L.D F2,45(R3)
L.D F6,34(R2)
Y
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
1 34+R2
2 45+R3
Dest
Reorder Buffer
Registers
L.D F6,34(R2)
L.D F2,45(R3)
MUL.D F0,F2,F4
SUB.D F8,F6,F2
DIV.D F10,F0,F6
ADD.D F6,F8,F2

## Slide 24: Speculation: Clock 3
3 MUL.D ROB2,F4
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
F2
F6
M(34+R2)
MUL.D F0,F2,F4
L.D F2,45(R3)
L.D F6,34(R2)
Y
Y
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
1 34+R2
2 45+R3
Dest
Reorder Buffer
Registers
L.D F6,34(R2)
L.D F2,45(R3)
MUL.D F0,F2,F4
SUB.D F8,F6,F2
DIV.D F10,F0,F6
ADD.D F6,F8,F2
Write Result

## Slide 25: Speculation: Clock 4-1
3 MUL.D ROB2,F4
4 SUB.D F6,BOB2
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F8
SUB.D F8,F6,F2
Y
F0
F2
F6
M(34+R2)
MUL.D F0,F2,F4
L.D F2,45(R3)
L.D F6,34(R2)
Y
Y
N
Busy?
Dest
Dest
Oldest
Newest
from
Memory
2 45+R3
Dest
Reorder Buffer
Registers
L.D F6,34(R2)
L.D F2,45(R3)
MUL.D F0,F2,F4
SUB.D F8,F6,F2
DIV.D F10,F0,F6
ADD.D F6,F8,F2
Committed
Write Result

## Slide 26: Speculation: Clock 4-2
3 MUL.D M(45+),F4 10
4 SUB.D F6, M(45+) 2
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F8
SUB.D F8,F6,F2
Y
F0
F2
M(45+)
MUL.D F0,F2,F4
L.D F2,45(R3)
Y
Y
N
Busy?
Dest
Dest
Oldest
Newest
from
Memory
2 45+R3
Dest
Reorder Buffer
Registers
L.D F6,34(R2)
L.D F2,45(R3)
MUL.D F0,F2,F4
SUB.D F8,F6,F2
DIV.D F10,F0,F6
ADD.D F6,F8,F2
Write Result
Start to run

## Slide 27: Speculation: Clock 5
3 MUL.D M(45+),F4 9
5 DIV.D ROB3,F6
4 SUB.D F6, M(45+) 1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F10
DIV.D F10,F0,F6
Y
F8
SUB.D F8,F6,F2
Y
F0
F2
M(45+)
MUL.D F0,F2,F4
L.D F2,45(R3)
Y
N
Busy?
Dest
Dest
Oldest
Newest
from
Memory
2 45+R3
Dest
Reorder Buffer
Registers
L.D F6,34(R2)
L.D F2,45(R3)
MUL.D F0,F2,F4
SUB.D F8,F6,F2
DIV.D F10,F0,F6
ADD.D F6,F8,F2
Committed

## Slide 28: Speculation: Clock 6
3 MUL.D M(45+),F4 8
5 DIV.D ROB3,F6
4 SUB.D F6, M(45+) 0
6 ADD.D ROB4,F2
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
SUB.D F8,F6,F2
Y
F0
MUL.D F0,F2,F4
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
L.D F6,34(R2)
L.D F2,45(R3)
MUL.D F0,F2,F4
SUB.D F8,F6,F2
DIV.D F10,F0,F6
ADD.D F6,F8,F2

## Slide 29: Speculation: Clock 7-1
3 MUL.D M(45+),F4 7
5 DIV.D ROB3,F6
4 SUB.D F6, M(45+)
6 ADD.D ROB4,F2
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
SUB.D F8,F6,F2
Y
F0
MUL.D F0,F2,F4
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Write Result

## Slide 30: Speculation: Clock 7-2
3 MUL.D M(45+),F4 7
5 DIV.D ROB3,F6
4 SUB.D F6, M(45+)
6 ADD.D F6-F2,F2 2
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
F6-F2
SUB.D F8,F6,F2
Y
F0
MUL.D F0,F2,F4
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Write Result

## Slide 31: Speculation: Clock 8
3 MUL.D M(45+),F4 6
5 DIV.D ROB3,F6
6 ADD.D F6-F2,F2 1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
F6-F2
SUB.D F8,F6,F2
Y
F0
MUL.D F0,F2,F4
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 32: Speculation: Clock 9
3 MUL.D M(45+),F4 5
5 DIV.D ROB3,F6
6 ADD.D F6-F2,F2 0
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
F6-F2
SUB.D F8,F6,F2
Y
F0
MUL.D F0,F2,F4
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 33: Speculation: Clock 10-1
3 MUL.D M(45+),F4 4
5 DIV.D ROB3,F6
6 ADD.D F6-F2,F2
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
F6-F2
SUB.D F8,F6,F2
Y
F0
MUL.D F0,F2,F4
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Write Result

## Slide 34: Speculation: Clock 10-2
3 MUL.D M(45+),F4 4
5 DIV.D ROB3,F6
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
F8+F2
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
F6-F2
SUB.D F8,F6,F2
Y
F0
MUL.D F0,F2,F4
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 35: Speculation: Clock 11-14
3 MUL.D M(45+),F4 0
5 DIV.D ROB3,F6
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
F8+F2
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
F6-F2
SUB.D F8,F6,F2
Y
F0
MUL.D F0,F2,F4
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 36: Speculation: Clock 15
3 MUL.D M(45+),F4
5 DIV.D F2*F4,F6 40
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
F8+F2
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
F6-F2
SUB.D F8,F6,F2
Y
F0
F2*F4
MUL.D F0,F2,F4
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Write Result

## Slide 37: Speculation: Clock 16
5 DIV.D F2*F4,F6 39
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
F8+F2
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
F6-F2
SUB.D F8,F6,F2
Y
F0
F2*F4
MUL.D F0,F2,F4
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Committed

## Slide 38: Speculation: Clock 17
5 DIV.D F2*F4,F6 38
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
F8+F2
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
F8
F6-F2
SUB.D F8,F6,F2
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Committed

## Slide 39: Speculation: Clock 18
5 DIV.D F2*F4,F6 37
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
F8+F2
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 40: Speculation: Clock 55
5 DIV.D F2*F4,F6 0
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
F8+F2
ADD.D F6,F8,F2
Y
F10
DIV.D F10,F0,F6
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 41: Speculation: Clock 56
5 DIV.D F2*F4,F6
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
F8+F2
ADD.D F6,F8,F2
Y
F10
F0/F6
DIV.D F10,F0,F6
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 42: Speculation: Clock 57
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
F8+F2
ADD.D F6,F8,F2
Y
F10
F0/F6
DIV.D F10,F0,F6
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Committed

## Slide 43: Speculation: Clock 58
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F6
F8+F2
ADD.D F6,F8,F2
Y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Committed

## Slide 44: Speculation: Clock 59
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 45: Speculation: Tables on the Book

## Slide 46: Speculation & Dynamic Scheduling
The important difference between speculation and only dynamic scheduling
  Speculation: SUB.D and ADD.D will not commit until MUL.D commits
  Dynamic scheduling: both the SUB.D and ADD.D have completed when MUL.D is ready to write its results

## Slide 47: Speculation: In-order Committing
No instruction after the earliest uncompleted instruction (MUL.D above) is allowed to complete (commit)
Maintaining a precise interrupt or precise exception

## Slide 48: Example II
Illustrate how the reorder buffer supports speculative execution
  Loop: L.D F0,0(R1)
  MUL.D F4,F0,F2
  S.D 0(R1),F4
  DADDIU R1,R1,#-8
  BNE R1,R2,Loop

## Slide 49: Example II: Assumptions
Issued all instructions in the loop twice
The L.D and MUL.D from the first iteration have committed
All other instructions have completed
The effective address for the store is computed by the time the instruction is issued
The store would wait in the ROB for both the effective address (R1) and the value (F4)

## Slide 50: Example II: Tables

## Slide 51: Example II: Undo
The processor can easily undo its speculative actions when a branch is found to be mispredicted
Because neither the register values nor any memory values are actually written until an instruction actually commits

## Slide 52: Example II: Branch Instruction
The branch BNE is not taken
  The instructions prior to the branch will commit when each reaches the head of the ROB
  When the branch reaches the head at the buffer, the buffer is simply cleared and the processor begins fetching instructions from the other path

## Slide 53: Steps of Speculation
Study the most details yourself!
  Next dozens of Project

## Slide 54: Issue
Wait until
  Reservation station (r) & ROB (b) both available

## Slide 55: Issue Bookkeeping 1/3: All Instructions
if (RegisterStat[rs].Busy)/*instr. wrts rs*/
  {h←RegisterStat[rs].Reorder;/*h is a temp var*/
  if (ROB[h].Ready)/*Instr completed*/
    {RS[r].Vj←ROB[h].Value; RS[r].Qj←0;}
  else {RS[r].Qj←h;} /*wait for instr result*/
}else {RS[r].Vj←Regs[rs]; RS[r].Qj←0;};
RS[r].Busy←yes; RS[r].Dest←b;
ROB[b].Instruction←opcode;
ROB[b].Dest←rd; ROB[b].Ready←no;

## Slide 56: Issue Bookkeeping 2/3: FPs and Stores
if (RegisterStat[rt].Busy) /*in-flight instr writes rt*/
  {h←RegisterStat[rt].Reorder;
  if (ROB[b].Ready) /*Instr completed*/
    {RS[r].Vk←ROB[h].Value; RS[r].Qk←0;}
  else {RS[r].Qk←h;} /*Wait for instr*/ }
else
  {RS[r].Vk←Regs[rt]; RS[r].Qk←0;};

## Slide 57: Issue Bookkeeping 3/3: Others
FP Operations
  RegisterStat[rd].Qi←b;
  RegisterStat[rd].Busy←yes;
  ROB[b].Dest←rd;
Loads
  RS[r].A←imm; RegisterStat[rt].Qi←b;
  RegisterStat[rt].Busy←yes; ROB[b].Dest←rt;
Stores
  RS[r].A←imm;

## Slide 58: Execute 1/2
FP Operations
  Wait until (RS[r].Qj=0) and (RS[r].Qk=0)
  Computing -- operands are in Vj and Vk
Load step 1
  Wait until (RS[r].Qj=0) & there are no stores earlier in the queue
  Bookkeeping
    RS[r].A←RS[r].Vj + RS[r].A;

## Slide 59: Execute 2/2
Load step 2
  Wait until Load step 1 done & all stores earlier in ROB have different address
  Bookkeeping
    Read from Mem[RS[r].A]
Store
  Wait until (RS[r].Qj=0) & store at queue head
  Bookkeeping
    ROB[h].Address←RS[r].Vj + RS[r].A;

## Slide 60: Write Results 1/2: All But Store
Execution done at r & CDB available
Bookkeeping
  b←RS[r].Reorder; RS[r].Busy←no;
  ∀x(if (RS[x].Qj=b) {RS[x].Vj←result; RS[x].Qj←0});
  ∀x(if (RS[x].Qk=b) {RS[x].Vk←result; RS[x].Qk←0});
  ROB[b].Value←result; ROB[b].Ready←yes;

## Slide 61: Write Results 2/2: Store
Wait until Execution done at r & (RS[r].Qk=0)
Bookkeeping
  ROB[h].Value←RS[r].Vk;

## Slide 62: Commit
Wait until
  Instruction is at the head of the ROB (entry h) and ROB[h].ready = yes

## Slide 63: Commit Bookkeeping 1/2
d←ROB[h].Dest; /*register dest, if exists*/
if (ROB[h].Instruction=Branch)
  {if (branch is mispredicted)
    {clear ROB[h].RegisterStat;
    fetch branch dest;};}
else if (ROB[h].Instruction=Store)
    {Mem[ROB[h].Address]←ROB[h].Value;}
  else /*put the result in the reg dest*/
    {Regs[r]←ROB[h].Value;};

## Slide 64: Commit Bookkeeping 2/2
ROB[h].Busy←no; /* free up ROB entry */
/* free up dest register if no one else writing it*/
if (RegisterStat[r].Qi=h)
  {RegisterStat[r].Busy←no;};

## Slide 65: Conclusion: Road Map
Instruction schedule
Loop-unrolling
Scoreboarding
Tomasulo’s algorithm
Speculation

## Slide 66: Next ...
3.7 Multiple Issue

## Slide 67: The VLIW
A LIW (Long Instruction Word) or a VLIW (Very Long instruction Word) architecture
The first commercial LIW processor was the AP-120B developed by Floating Point Systems
A later model, the FPS-164, had 10 instructions per wide word for 10 separate functional units

## Slide 68: Rely on VLIW Compiler Technology
To minimize the potential data hazard stalls
To actually format the instructions in a potential issue packet
  It issue a package of instructions within the fields rather than trying to issue multiple independent instructions to the units

## Slide 69: The VLIW Compiler Must…
The VLIW hardware need not check explicitly for dependences
To ensure that dependences within the issue packet cannot be present or
At a minimum, indicate when a dependence may be present

## Slide 70: The Potential Advantages of VLIW
Simpler hardware
Still exhibiting good performance through extensive compiler optimization
The VLIW organization
  Uses multiple independent units
  Packages the multiple operations into one long instruction word

## Slide 71: The VLIW Instructions
A VLIW instruction would have a set of fields for each functional unit
  Perhaps 16 to 24 bits per unit
It might include following seven units
  Two integers
  Two floating-points
  Two memory references
  A branch
An instruction length from 112 to 168 bits

## Slide 72: Early VLIWs: Quite Rigid
The hardware simply sends the appropriate fields to the FUs
The compiler is responsible for
  Keeping each FU is busy for each cycle
  Putting in a NOP for any unit that has no work to do
Effectively required re-compile of programs for different versions of the hardware

## Slide 73: Recent Architectures
Still requiring the compiler to do most of the work of finding and scheduling instructions for parallel execution
Being pursued for desktop and server markets
  Transmeta (bankrupt) Crusoe (The hero of the England writer Defoe’s Robinson Crusoe)
  Intel Itanium

## Slide 74: A VLIW Example
Scheduling the loop for a VLIW machine with
  Two memory references
  Two FP operations
  One integer/branch operation
Gives us the following code sequence:
  Loop x[i] = x[i] + s

## Slide 75: The VLIW Example Code
  Loop: L.D F0,0(R1)
  ADD.D F4,F0,F2
  S.D F4,0(R1)
  DADDUI R1,R1,#-8
  BNE R1,R2,Loop
The loop has been unrolled to make seven copies of the body

## Slide 76: The VLIW Example Execution
Mem Ref1 | Mem Ref2 | FP1 | FP2 | Int/branch
L.D F0,0(R1) | L.D F6,-8(R1) |  |  | 
L.D F10,-16(R1) | L.D F14,-24(R1) |  |  | 
L.D F18,-32(R1) | L.D F22,-40(R1) | ADD.D F4,F0,F2 | ADD.D F8,F6,F2 | 
L.D F26,-48(R1) |  | ADD.D F12,F10,F2 | ADD.D F16,F14,F2 | 
 |  | ADD.D F20,F18,F2 | ADD.D F24,F22,F2 | 
S.D F4,0(R1) | S.D F8,-8(R1) | ADD.D F28,F26,F2 |  | 
S.D F12,-16(R1) | S.D F16,-24(R1) |  |  | DADDUI R1,R1,#-56
S.D F20,24(R1) | S.D F24,16(R1) |  |  | 
S.D F28,8(R1) |  |  |  | BNE R1,R2,Loop
7 results in 9 cycles, or 1.29 cycles per result
The issue rate is 23 operations in 9 clock cycles
  2.5 operations/cycle

## Slide 77: The VLIW Example Performance
1.29 cycles per result
  Nearly twice as fast as the two-issue static superscalar (2.4 clock cycles per element, see F4.2/p313)
2.5 operations per cycle
  The efficiency, the used slots, is about 51% (23/45)

## Slide 78: The Registers in VLIW Example
It requires a larger number of registers than MIPS would normally use
  2*7+1=15 FP regs
The base MIPS use only 3 (2*1+1) FP registers
  See the code in p305
In the superscalar example 11 (2*5+1) registers were needed

## Slide 79: The VLIW without Empty Issue
Mem Ref1 | Mem Ref2 | FP1 | FP2 | Int/branch
L.D F0,0(R1) | L.D F6,-8(R1) |  |  | 
L.D F10,-16(R1) |  |  |  | 
 |  | ADD.D F4,F0,F2 | ADD.D F8,F6,F2 | 
 |  | ADD.D F12,F10,F2 |  | 
 |  |  |  | DADDUI R1,R1,#-24
S.D F4,24(R1) | S.D F8,16(R1) |  |  | 
S.D F12,8(R1) |  |  |  | 
 |  |  |  | BNE R1,R2,Loop
3 results in 8 cycles, or 2.66 cycles per result
Efficiency of operation slot: 11/40 = 27.5%

## Slide 80: The VLIW without Empty FP-op
Mem Ref1 | Mem Ref2 | FP1 | FP2 | Int/branch
L.D F0,0(R1) | L.D F6,-8(R1) |  |  | 
L.D F10,-16(R1) | L.D F14,-24(R1) |  |  | 
L.D F18,-32(R1) | L.D F22,-40(R1) | ADD.D F4,F0,F2 | ADD.D F8,F6,F2 | 
L.D F26,-48(R1) | L.D F30,-56(R1) | ADD.D F12,F10,F2 | ADD.D F16,F14,F2 | 
L.D F34,-64(R1) | L.D F38,-72(R1) | ADD.D F20,F18,F2 | ADD.D F24,F22,F2 | DADDUI R1,R1,#-80
S.D F4,80(R1) | S.D F8,72(R1) | ADD.D F28,F26,F2 | ADD.D F32,F30,F2 | 
S.D F12,64(R1) | S.D F16,56(R1) | ADD.D F36,F34,F2 | ADD.D F40,F38,F2 | 
S.D F20,48(R1) | S.D F20,40(R1) |  |  | 
S.D F20,32(R1) | S.D F20,24(R1) |  |  | 
S.D F20,16(R1) | S.D F20,8(R1) |  |  | BNE R1,R2,Loop
10 results in 10 cycles with 42 FP registers (if available), or 1.00 cycles per result
Efficiency of operation slot: 36/50 =72%

## Slide 81: Problems Of VLIW
The technical problems
  The increase in code size
  And the limitations of lock-step operation
A major logistical problem
  Binary code compatibility

## Slide 82: Two Reasons to Increase Code Size
A vast amount of independent operations
  Generating operations in a straight-line code fragment requires ambitiously unrolling loops
  >Exploiting large amounts of ILP
Low efficiency usage of FUs
  The unused functional units translate to wasted bits in the instruction encoding
  In previous example, about 51% of the functional units were used

## Slide 83: Decrease VLIW Code Size
Set one large immediate field for use by any functional unit
Compress the instructions in main memory and expand them when they are read into the cache or are decoded
  By hardware

## Slide 84: VLIW’s Lock-step Operation
Lock-step: all the FUs must synchronize
There was no hazard detection hardware
A stall in any FU must cause the entire processor to stall

## Slide 85: Long Lock-step: Memory Reference
Predicting which data will encounter a cache stall and scheduling them is very difficult
As the issue rate and number of memory references becomes large, this synchronization restriction becomes unacceptable

## Slide 86: VLIW’s Lock-step Under H/W
In more recent processors, the functional units operate more independently
The compiler is used to avoid hazards at issue time
Hardware checks allow for unsynchronized execution once instructions are issued
  Dynamic VLIW approach

## Slide 87: Binary Code Compatibility
A VLIW code sequence is decided by
  The instruction set
  The detailed pipeline structure
  FUs and their latencies
Different numbers of FUs and unit latencies require different versions of the code
  The ability to run old binary files is an advantage of the superscalar

## Slide 88: Solution to Code Migration
Object-code translation or emulation
  This technology is developing quickly and could play a significant role in future migration schemes
Temper the strictness
  So that binary compatibility is still feasible
  This approach is used in the IA-64

## Slide 89: The Future of VLIW
Some vendors are betting VLIW is the future
  Intel/HP has stated that they will use VLIW-like for Merced core instead of the RISC core of the Pentium Pro, the Pentium II, III, and 4
  Transmeta is using VLIW in the Crusoe microprocessors
Many now architectures use the features of VLIW, or use VLIW in calculate unit

## Slide 90: Next …
Super Scale