## Slide 1: Advanced Computer Architecture (ACA2020)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2020

## Slide 2: Lecture 10 Vector Processor, SIMD and GPU

## Slide 3: Chapter 4 DLP in Vector, SIMD, and GPU
Data-Level Parallelism in Vector, SIMD, and GPU Architectures (pp262-334)
  4.1 Introduction
  4.2 Vector Architecture
  4.3 SIMD Instruction Set Extensions for Multimedia
  4.4 Graphics Processing Units
  4.5 Detecting and Enhancing Loop-Level Parallelism
  4.6 Crosscutting Issues
  4.7 Putting It All Together: Mobile versus Server GPUs and Tesla versus Core i7

## Slide 4: App G. Vector Processors in More Depth
G.1 Introduction
G.2 Vector Performance in More Depth
G.3 Vector Memory Systems in More Depth
G.4 Enhancing Vector Performance
G.5 Effectiveness of Compiler Vectorization
G.6 Putting It All Together: Performance of Vector Processors
G.7 A Modern Vector Supercomputer: The Cray X1

## Slide 5: SIMD Parallelism
Vector architectures
SIMD extensions
Graphics Processor Units (GPUs)

## Slide 6: Vector Architectures
The most efficient way to execute a vectorizable application is a vector processor. Jim Smith, ISCA (1994)
Basic idea:
  Read sets of data elements into “vector registers”
  Operate on those registers
  Disperse the results back into memory
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth

## Slide 7: Supercomputer Applications
Typical application areas
  Military research (nuclear weapons, cryptography)
  Scientific research
  Weather forecasting
  Oil exploration
  Industrial design (car crash simulation)
  Bioinformatics
  Cryptography
All involve huge computations on large data set
Supercomputers: CDC6600, CDC7600, Cray-1, …
In 70s-80s, Supercomputer  Vector Machine

## Slide 8: Vector Supercomputers
Cray-1, 1976
Scalar Unit
  Load/Store Architecture
Vector Extension
  Vector Registers
  Vector Instructions
Implementation
  Hardwired Control
  Highly Pipelined Functional Units
  Interleaved Main Memory System
  No Data Caches
    Local memory
  No Virtual Memory
[©Cray Research, 1976]

## Slide 9: Vector Programming Model
+
+
+
+
+
+
[0]
[1]
[VLR-1]
Vector Arithmetic Instructions
vadd v3, v1, v2
v3
v2
v1
Scalar Registers
x0
x31
Vector Registers
v0
v31
[0]
[1]
[2]
[VLRMAX-1]
VLR
Vector Length Register
v1
Vector Load and Store Instructions
vld v1, x1, x2
Base, x1
Stride, x2
Memory
Vector Register

## Slide 10: Vector Code Example
# Scalar Code
li x4, 64
loop:
fld f1, 0(x1)
fld f2, 0(x2)
fadd.d f3,f1,f2
fsd f3, 0(x3)
addi x1, 8
addi x2, 8
addi x3, 8
subi x4, 1
bnez x4, loop
# Vector Code
li x4, 64
setvlr x4
vfld v1, x1
vfld v2, x2
vfadd.d v3,v1,v2
vfsd v3, x3
# C code
for (i=0; i<64; i++)
C[i] = A[i] + B[i];

## Slide 11: Cray-1 (1976)
Single Port
Memory
16 banks of 64-bit words
+
8-bit SECDED
80MW/sec data load/store
320MW/sec instruction
buffer refill
4 Instruction Buffers
64-bitx16
NIP
LIP
CIP
(A0)
( (Ah) + j k m )
64
T Regs
(A0)
( (Ah) + j k m )
64
B Regs
S0
S1
S2
S3
S4
S5
S6
S7
A0
A1
A2
A3
A4
A5
A6
A7
Si
Tjk
Ai
Bjk
FP Add
FP Mul
FP Recip
Int Add
Int Logic
Int Shift
Pop Cnt
Sj
Si
Sk
Addr Add
Addr Mul
Aj
Ai
Ak
memory bank cycle 50 ns processor cycle 12.5 ns (80MHz)
V0
V1
V2
V3
V4
V5
V6
V7
Vk
Vj
Vi
V. Mask
V. Length
64 Element Vector Registers

## Slide 12: Vector Instruction Set Advantages
Compact
  one short instruction encodes N operations
Expressive, tells hardware that these N operations:
  are independent
  use the same functional unit
  access disjoint registers
  access registers in same pattern as previous instructions
  access a contiguous block of memory (unit-stride load/store)
  access memory in a known pattern (strided load/store)
Scalable
  can run same code on more parallel pipelines (lanes)
2020/12/16

## Slide 13: Vector Arithmetic Execution
Use deep pipeline (=> fast clock) to execute element operations
Simplifies control of deep pipeline because elements in vector are independent (=> no hazards!)
v1
v2
v3
v3 <- v1 * v2
Six-stage multiply pipeline

## Slide 14: Vector Instruction Execution
vfadd.d vc, va, vb
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units

## Slide 15: Interleaved Vector Memory System
Bank busy time: Time before bank ready to accept next request
Cray-1, 16 banks, 4 cycle bank busy time, 12 cycle latency
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator
2020/12/16

## Slide 16: Vector Unit Structure
Lane
Functional Unit
Vector
Registers
Memory Subsystem
Elements 0, 4, 8, …
Elements 1, 5, 9, …
Elements 2, 6, 10, …
Elements 3, 7, 11, …

## Slide 17: Vector Instruction Parallelism
Can overlap execution of multiple vector instructions
  example machine has 32 elements per vector register and 8 lanes
load
load
mul
mul
add
add
Load Unit
Multiply Unit
Add Unit
time
Instruction issue
Complete 24 operations/cycle while issuing 1 short instruction/cycle
2020/12/16

## Slide 18: Vector Chaining
Vector version of register bypassing
  introduced with Cray-1
Memory
V1
Load Unit
Mult.
V2
V3
Chain
Add
V4
V5
Chain
vld v1
vfmul v3,v1,v2
Vfadd v5, v3, v4

## Slide 19: Vector Chaining Advantage
Without chaining, must wait for last element of result to be written before starting dependent instruction
With chaining, can start dependent instruction as soon as first result appears
Load
Mul
Add
Load
Mul
Add
Time

## Slide 20: Vector Startup
Two components of vector startup penalty
  functional unit latency (time through pipeline)
  dead time or recovery time (time before another vector instruction can start down pipeline)
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
R
X
X
X
W
Functional Unit Latency
Dead Time
First Vector Instruction
Second Vector Instruction
Dead Time

## Slide 21: Dead Time and Short Vectors
T0, Eight lanes
No dead time
100% efficiency with 8 element vectors
No dead time
Cray C90, Two lanes
4 cycle dead time
Maximum efficiency 94% with 128 element vectors
4 cycles dead time
64 cycles active

## Slide 22: Vector Memory-Memory versus Vector Register Machines
Vector memory-memory instructions hold all vector operands in main memory
The first vector machines, CDC Star-100 (‘73) and TI ASC (‘71), were memory-memory machines
Cray-1 (’76) was first vector register machine
for (i=0; i<N; i++)
{
C[i] = A[i] + B[i];
D[i] = A[i] - B[i];
}
Example Source Code
ADDV C, A, B
SUBV D, A, B
Vector Memory-Memory Code
LV V1, A
LV V2, B
ADDV V3, V1, V2
SV V3, C
SUBV V4, V1, V2
SV V4, D
Vector Register Code

## Slide 23: Vector Memory-Memory vs. Vector Register Machines
Vector memory-memory architectures (VMMA) require greater main memory bandwidth, why?
  All operands must be read in and out of memory
VMMAs make if difficult to overlap execution of multiple vector operations, why?
  Must check dependencies on memory addresses
VMMAs incur greater startup latency
  Scalar code was faster on CDC Star-100 for vectors < 100 elements
  For Cray-1, vector/scalar breakeven point was around 2-4 elements
Apart from CDC follow-ons (Cyber-205, ETA-10) all major vector machines since Cray-1 have had vector register architectures
(we ignore vector memory-memory from now on)

## Slide 24: Automatic Code Vectorization
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vectorization is a massive compile-time reordering of operation sequencing
 requires extensive loop dependence analysis
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time

## Slide 25: Vector Stripmining
Problem: Vector registers have finite length
Solution: Break loops into pieces that fit in registers, “Stripmining”
andi x1, xN, 63 # N mod 64
setvlr x1 # Do remainder
loop:
vld v1, xA
sll x2, x1, 3 # Multiply by 8
add xA, x2 # Bump pointer
vld v2, xB
add xB, x2
vfadd.d v3, v1, v2
vsd v3, xC
add xC, x2
sub xN, x1 # Subtract elements
li x1, 64
setvlr x1 # Reset full length
bgtz xN, loop # Any more to do?
for (i=0; i<N; i++)
C[i] = A[i]+B[i];
+
+
+
A
B
C
64 elements
Remainder
2020/12/16

## Slide 26: Vector Conditional Execution
Problem: Want to vectorize loops with conditional code:
      for (i=0; i<N; i++)
      if (A[i]>0) then
      A[i] = B[i];
Solution: Add vector mask (or flag) registers
  vector version of predicate registers, 1 bit per element
…and maskable vector instructions
  vector operation becomes bubble (“NOP”) at elements where mask bit is clear
Code example:
  cvm # Turn on all elements
  vld vA, xA # Load entire A vector
  vfsgts.d vA, f0 # Set bits in mask register where A>0
  vld vA, xB # Load B vector into A under mask
  vsd vA, xA # Store A back to memory under mask

## Slide 27: Masked Vector Instructions
C[4]
C[5]
C[1]
Write data port
A[7]
B[7]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
Density-Time Implementation
  scan mask vector and only execute elements with non-zero masks
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
Write data port
Write Enable
A[7]
B[7]
M[7]=1
Simple Implementation
  execute all N operations, turn off result writeback according to mask

## Slide 28: Compress/Expand Operations
Compress packs non-masked elements from one vector register contiguously at start of destination vector register
  population count of mask vector gives packed vector length
Expand performs inverse operation
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
A[3]
A[4]
A[5]
A[6]
A[7]
A[0]
A[1]
A[2]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
B[3]
A[4]
A[5]
B[6]
A[7]
B[0]
A[1]
B[2]
Expand
A[7]
A[1]
A[4]
A[5]
Compress
A[7]
A[1]
A[4]
A[5]
Used for density-time conditionals and also for general selection operations

## Slide 29: Vector Reductions
Problem: Loop-carried dependence on reduction variables
  sum = 0;
  for (i=0; i<N; i++)
  sum += A[i]; # Loop-carried dependence on sum
Solution: Re-associate operations if possible, use binary tree to perform reduction
  # Rearrange as:
  sum[0:VL-1] = 0 # Vector of VL partial sums
  for(i=0; i<N; i+=VL) # Stripmine VL-sized chunks
  sum[0:VL-1] += A[i:i+VL-1]; # Vector sum
  # Now have VL partial sums in one vector register
  do {
  VL = VL/2; # Halve vector length
  sum[0:VL-1] += sum[VL:2*VL-1] # Halve no. of partials
  } while (VL>1)

## Slide 30: Vector Scatter/Gather
Want to vectorize loops with indirect accesses:
  for (i=0; i<N; i++)
  A[i] = B[i] + C[D[i]]
Indexed load instruction (Gather)
  vld vD, xD # Load indices in D vector
  vdli vC, xC, vD # Load indirect from rC base
  vld vB, xB # Load B vector
  vfadd.d vA,vB,vC # Do add
  vsd vA, xA # Store result

## Slide 31: Vector Scatter/Gather
Histogram example:
  for (i=0; i<N; i++)
  A[B[i]]++;
Is following a correct translation?
  vld vB, xB # Load indices in B vector
  vldi vA, xA, vB # Gather initial A values
  vadd vA, vA, 1 # Increment
  vsdi vA, xA, vB # Scatter incremented values

## Slide 32: Vector Memory Models
Most vector machines have a very relaxed memory model, e.g.
  vsd v1, x1 # Store vector to x1
  vld v2, x1 # Load vector from x1
  No guarantee that elements of v2 will have value of elements of v1 even when store and load execute by same processor!
Requires explicit memory barrier or fence
  vsd v1, x1 # Store vector to x1
  fence.vs.vl # Enforce ordering s->l
  vld v2, x1 # Load vector from x1
Vector machines support highly parallel memory systems (multiple lanes and multiple load and store units) with long latency (100+ clock cycles)
  hardware coherence checks would be prohibitively expensive
  vectorizing compiler can eliminate most dependencies

## Slide 33: A Recent Vector Super: NEC SX-9 (2008)
65nm CMOS technology
Vector unit (3.2 GHz)
  8 foreground VRegs + 64 background VRegs (256x64-bit elements/VReg)
  64-bit functional units: 2 multiply, 2 add, 1 divide/sqrt, 1 logical, 1 mask unit
  8 lanes (32+ FLOPS/cycle, 100+ GFLOPS peak per CPU)
  1 load or store unit (8 x 8-byte accesses/cycle)
Scalar unit (1.6 GHz)
  4-way superscalar with out-of-order and speculative execution
  64KB I-cache and 64KB data cache
Memory system provides 256GB/s DRAM bandwidth per CPU
Up to 16 CPUs and up to 1TB DRAM form shared-memory node
  total of 4TB/s bandwidth to shared DRAM memory
Up to 512 nodes connected via 128GB/s network links (message passing between nodes)
[ ©NEC ]
[ New announcement SX-ACE, 4x16-lane vector CPUs on one chip]
Notes: Picture from NEC article “A hardware overview of SX-6 and SX-7 supercomputer”

## Slide 34: Memory Banks Example: Cray T90 (Cray T932)
32 processors, each generating 4 loads and 2 stores/cycle
Clock cycle is 2.167 ns, SRAM cycle is 15 ns
How many memory banks needed?
Answer
  The maximum number of memory references each cycle is 192: 32 processors times 6 references per processor
  Each SRAM bank is busy for 15/2.167 = 6.92 clock cycles, which we round up to 7 processor clock cycles
  We require a minimum of 192 × 7 = 1344 memory banks
  The Cray T932 actually has 1024 memory banks

## Slide 35: Programming Vector Architectures
Compilers can provide feedback
Programmers can provide hints to compiler

## Slide 36: Seymour Cray’s Lecture
I’m certainly not inventing vector processors. There are three kinds that I know of existing today. They are represented by the Illiac-IV, the (CDC) Star processor, and the TI (ASC) processor
Those three were all pioneering processors. . . . One of the problems of being a pioneer is you always make mistakes and I never, never want to be a pioneer
It’s always best to come second when you can look at the mistakes the pioneers made
1976

## Slide 37: Vector Summary
Vector is alternative model for exploiting ILP
If code is vectorizable, then simpler hardware, more energy efficient, and better real-time model than Out-of-order machines
Design issues include number of lanes, number of functional units, number of vector registers, length of vector registers, exception handling, conditional operations
Fundamental design issue is memory bandwidth
Will multimedia popularity revive vector architectures?

## Slide 38: Next…
SIMD processing

## Slide 39: For x86 Computers
Potential speedup via parallelism from MIMD, SIMD, and both MIMD and SIMD over time
  Expect two additional cores per chip per year
  SIMD width to double every four years
  Potential speedup from SIMD to be twice that from MIMD!

## Slide 40: SIMD Extensions
Media applications operate on data types narrower than the native word size
  Example: disconnect carry chains to “partition” adder
Limitations, compared to vector instructions:
  Number of data operands encoded into op code
  No sophisticated addressing modes (strided, scatter-gather)
  No mask registers

## Slide 41: SIMD Implementations
Intel MMX (1996)
  Eight 8-bit integer ops or four 16-bit integer ops
  Operands must be consecutive and aligned memory locations
Streaming SIMD Extensions (SSE) (1999)
  Eight 16-bit integer ops
  Four 32-bit integer/fp ops or two 64-bit integer/fp ops
Advanced Vector eXtensions (AVX) (2010)
  Four 64-bit integer/fp ops

## Slide 42: Multimedia Extensions
Very short vectors existing ISAs for micros
  Usually 64-bit registers split into 2x32b or 4x16b or 8x8b
  Newer designs have 128-bit registers (Altivec, SSE2)
Limited instruction set:
  no vector length control
  no strided load/store or scatter/gather
  unit-stride loads must be aligned to 64/128-bit boundary

## Slide 43: Multimedia Extensions
Limited vector register length:
  requires superscalar dispatch to keep multiply/add/load units busy
  loop unrolling to hide latencies increases register pressure
Trend towards fuller vector support in microprocessors

## Slide 44: MMX Instructions
Move 32b, 64b
Add, Subtract in parallel: 8*8b, 4*16b, 2*32b
  opt. signed/unsigned saturate (set to max) if overflow
Shifts (sll,srl, sra), And, And Not, Or, Xor in parallel: 8*8b, 4*16b, 2*32b
Multiply, Multiply-Add in parallel: 4*16b
Compare = , > in parallel: 8*8b, 4*16b, 2*32b
  sets field to 0s (false) or 1s (true); removes branches
Pack/Unpack
  Convert 32b<–> 16b, 16b <–> 8b
  Pack saturates (set to max) if number is too large

## Slide 45: Example SIMD Code: DXPY
  L.D F0,a ;load scalar a
  MOV F1, F0 ;copy a into F1 for SIMD MUL
  MOV F2, F0 ;copy a into F2 for SIMD MUL
  MOV F3, F0 ;copy a into F3 for SIMD MUL
  DADDIU R4,Rx,#512 ;last address to load
  Loop: L.4D F4,0[Rx] ;load X[i], X[i+1], X[i+2], X[i+3]
  MUL.4D F4,F4,F0 ;a×X[i],a×X[i+1],a×X[i+2],a×X[i+3]
  L.4D F8,0[Ry] ;load Y[i], Y[i+1], Y[i+2], Y[i+3]
  ADD.4D F8,F8,F4 ;a×X[i]+Y[i], ..., a×X[i+3]+Y[i+3]
  S.4D 0[Ry],F8 ;store into Y[i], Y[i+1], Y[i+2], Y[i+3]
  DADDIU Rx,Rx,#32 ;increment index to X
  DADDIU Ry,Ry,#32 ;increment index to Y
  DSUBU R20,R4,Rx ;compute bound
  BNEZ R20,Loop ;check if done
The multiply MUL.4D does F4*F0, F5*F1, F6*F2, and F7*F3

## Slide 46: Roofline Performance Model
Basic idea:
  Plot peak floating-point throughput as a function of arithmetic intensity
  Ties together floating-point performance and memory performance for a target machine
Arithmetic intensity
  Floating-point operations per byte read

## Slide 47: Roofline Performance Model

## Slide 48: Examples
Attainable GFLOPs/sec Min = (Peak Memory BW × Arithmetic Intensity, Peak Floating Point Perf.)

## Slide 49: Next…
Graphics Processing Units (GPU)

## Slide 50: Graphical Processing Units
Given the hardware invested to do graphics well
  How can be supplement it to improve performance of a wider range of applications?
Basic idea:
  Heterogeneous execution model
    CPU is the host, GPU is the device
  Develop a C-like programming language for GPU
    Unify all forms of GPU parallelism as CUDA thread
  Programming model is “Single Instruction Multiple Thread”

## Slide 51: Threads and Blocks
A thread is associated with each data element
Threads are organized into blocks
  These threads are blocked together and executed in groups of 32 threads, called a Thread Block
  GPU hardware handles thread management, not applications or OS
Blocks are organized into a grid
The hardware that executes a whole block of threads a multithreaded SIMD Processor

## Slide 52: NVIDIA GPU Architecture
Similarities to vector machines:
  Works well with data-level parallel problems
  Scatter-gather transfers
  Mask registers
  Large register files
Differences:
  No scalar processor
  Uses multithreading to hide memory latency
  Has many functional units, as opposed to a few deeply pipelined units like a vector processor

## Slide 53: Few Details of a CUDA Program
CUDA functions
  for the GPU (device) uses __device__ or __global__
  for the system processor (host) uses __host__
CUDA GPU Memory variables declared as in the __device__ or __global__functions
  Accessible by all multithreaded SIMD processors.
The function name that runs on the GPU is
  name<<<dimGrid, dimBlock>>>(... parameter list ...)
  dimGrid: dimensions of the code (in blocks)
  dimBlock: dimensions of a block (in threads)
The identifier for blocks ( blockIdx )
The identifier for threads per block ( threadIdx ),
The number of threads per block ( blockDim )
  Which comes from the dimBlock parameter in the bullet above

## Slide 54: DAXPY
Conventional C code
  // DAXPY in C
  void daxpy(int n,
  double a,
  double *x,
  double *y)
  {
  for (int i = 0; i < n; ++i)
  y[i] = a*x[i] + y[i];
  }
  // Perform SAXPY on 1M elements
  daxpy (4096*256, 2.0, x, y);
The CUDA version
  // DAXPY in CUDA
  __device__
  //__Global__
  void daxpy(int n,
  double a,
  double *x,
  double *y)
  {
  int i = blockIdx.x*blockDim.x + threadIdx.x;
  if (i < n) y[i] = a*x[i] + y[i];
  }
  // Perform SAXPY on 1M elements
  daxpy<<<4096,256>>>(n, 2.0, x, y);

## Slide 55: GPU terms in book and NVIDIA and OpenCL - 1

## Slide 56: GPU terms in book and NVIDIA and OpenCL - 2

## Slide 57: GPU terms in book and NVIDIA and OpenCL – 1 ( from back cover)

## Slide 58: GPU terms in book and NVIDIA and OpenCL - 2 ( from back cover)

## Slide 59: Grid, Thread Blocks and SIMD Threads
The mapping of a Grid (vectorizable loop), Thread Blocks (SIMD basic blocks), and threads of SIMD instructions
  The GPU code that works on the whole 8192 element multiply is called a Grid (or vectorized loop)
  A Grid is composed of Thread Blocks (or body of a vectorized loop), each with up to 512 elements
  A SIMD instruction (Thread) executes 32 elements at a time

## Slide 60: Example: Multiply two vectors of length 8192
A Thread Block is assigned to a processor that executes that code, which we call a multithreaded SIMD Processor, by the Thread Block Scheduler
The Thread Block Scheduler has some similarities to a control processor in a vector architecture
It determines the number of thread blocks needed for the loop and keeps allocating them to different multithreaded SIMD Processors until the loop is completed
In this example, it would send 16 Thread Blocks to multithreaded SIMD Processors to compute all 8192 elements of this loop
Current-generation GPUs (Fermi) have 7-15 multithreaded SIMD processors

## Slide 61: Kepler GK110 Full Chip Block Diagram

## Slide 62: Streaming Multiprocessor (SMX) Architecture
SMX: 192 single-precision CUDA cores, 64 double-precision units, 32 special function units (SFU), and 32 load/store units (LD/ST)

## Slide 63: A Multithreaded SIMD Processor
16 SIMD lanes
The SIMD Thread Scheduler has, say, 48 independent threads of SIMD instructions that it schedules with a table of 48 PCs

## Slide 64: Terminology
Threads of SIMD instructions
  Each has its own PC
  Thread scheduler uses scoreboard to dispatch
  No data dependencies between threads!
  Keeps track of up to 48 threads of SIMD instructions
    Hides memory latency
Thread block scheduler schedules blocks to SIMD processors
Because threads of SIMD instructions are independent, the scheduler may select a different SIMD thread each time

## Slide 65: Example
NVIDIA GPU has 32,768 registers
  Divided into lanes
  Each SIMD thread is limited to 64 registers
  SIMD thread has up to:
    64 vector registers of 32 32-bit elements
    32 vector registers of 32 64-bit elements
  Fermi has 16 physical SIMD lanes, each containing 2048 registers

## Slide 66: NVIDIA Instruction Set Architecture
ISA is an abstraction of the hardware instruction set
  “Parallel Thread Execution (PTX)”
  Uses virtual registers
  Translation to machine code is performed in software

## Slide 67: Basic PTX GPU Thread Instructions

## Slide 68: DAXPY Example
shl.s32 R8, blockIdx, 9
add.s32 R8, R8, threadIdx
ld.global.f64 RD0, [X+R8]
ld.global.f64 RD2, [Y+R8]
mul.f64 R0D, RD0, RD4
add.f64 R0D, RD0, RD2
st.global.f64 [Y+R8], RD0
; Thread Block ID * Block size (512 or 29)
; R8 = i = my CUDA thread ID
; RD0 = X[i]
; RD2 = Y[i]
; Product in RD0 = RD0 * RD4 (scalar a)
; Sum in RD0 = RD0 + RD2 (Y[i])
; Y[i] = sum (X[i]*a + Y[i])

## Slide 69: Loop-Level Parallelism
Focuses on determining whether data accesses in later iterations are dependent on data values produced in earlier iterations
  Loop-carried dependence
Example 1:
for (i=999; i>=0; i=i-1)
x[i] = x[i] + s;
No loop-carried dependence

## Slide 70: Loop-Level Parallelism
Example 2:
for (i=0; i<100; i=i+1) {
A[i+1] = A[i] + C[i]; /* S1 */
B[i+1] = B[i] + A[i+1]; /* S2 */
}
S1 and S2 use values computed by S1 in previous iteration
S2 uses value computed by S1 in same iteration

## Slide 71: Loop-Level Parallelism
Example 3:
for (i=0; i<100; i=i+1) {
A[i] = A[i] + B[i]; /* S1 */
B[i+1] = C[i] + D[i]; /* S2 */
}
S1 uses value computed by S2 in previous iteration but dependence is not circular so loop is parallel
Transform to:
A[0] = A[0] + B[0];
for (i=0; i<99; i=i+1) {
B[i+1] = C[i] + D[i];
A[i+1] = A[i+1] + B[i+1];
}
B[100] = C[99] + D[99];

## Slide 72: Loop-Level Parallelism
Example 4:
for (i=0;i<100;i=i+1) {
A[i] = B[i] + C[i];
D[i] = A[i] * E[i];
}
Example 5:
for (i=1;i<100;i=i+1) {
Y[i] = Y[i-1] + Y[i];
}

## Slide 73: Finding Dependencies
Assume indices are affine:
  a x i + b (i is loop index)
Assume:
  Store to a x i + b, then
  Load from c x i + d
  i runs from m to n
  Dependence exists if:
    Given j, k such that m ≤ j ≤ n, m ≤ k ≤ n
    Store to a x j + b, load from a x k + d, and a x j + b = c x k + d

## Slide 74: Finding Dependencies
Generally cannot determine at compile time
Test for absence of a dependence:
  GCD test:
    If a dependency exists, GCD(c,a) must evenly divide (d-b)
Example:
  for (i=0; i<100; i=i+1) {
  X[2*i+3] = X[2*i] * 5.0;
  }

## Slide 75: Finding Dependencies
Example 2:
  for (i=0; i<100; i=i+1) {
  Y[i] = X[i] / c; /* S1 */
  X[i] = X[i] + c; /* S2 */
  Z[i] = Y[i] + c; /* S3 */
  Y[i] = c - Y[i]; /* S4 */
  }
Watch for antidependencies and output dependencies

## Slide 76: Reductions
Reduction Operation:
for (i=9999; i>=0; i=i-1)
sum = sum + x[i] * y[i];
Transform to…
for (i=9999; i>=0; i=i-1)
sum [i] = x[i] * y[i];
for (i=9999; i>=0; i=i-1)
finalsum = finalsum + sum[i];
Do on p processors:
for (i=999; i>=0; i=i-1)
finalsum[p] = finalsum[p] + sum[i+1000*p];
Note: assumes associativity!

## Slide 77: Homework
Review
  4.1~4.4
  G.1~G.5
Reading papers
  The CRAY-1 Computer System