## Slide 1: Advanced Computer Architecture (ACA2020)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2020

## Slide 2: Lecture 12 Thread-Level Parallelism - TLP

## Slide 3: 3.12 TLP
Multithreading: Exploiting Thread-Level Parallelism to Improve Uniprocessor Throughput
A thread: a separate process with own instructions and data
  Each thread has all the state necessary to allow it to execute
  Thread state
    instructions, data, PC, register state, and so on
  There can be much higher natural parallelism in some applications
    e.g., database or scientific codes

## Slide 4: Thread Level Parallelism (TLP)
TLP is program can logically structured as separate threads of execution
TLP is explicitly represented by the use of multiple threads of execution that are inherently parallel
  What is a ILP?
  ILP exploits implicit parallel operations
  TLP could be more cost-effective than ILP
TLP, multiple instruction streams to improve
  Throughput that run many programs
  Execution time of multi-threaded programs

## Slide 5: Multithreaded Execution
For running independent programs, the processor must duplicate independent state of each thread e.g.
  a separate copy of register file
  a separate PC
  a separate page table
Memory shared through the virtual memory mechanisms which already support multiple processes

## Slide 6: Multithreaded Switch
HW for fast thread switch
  Usually done in a round-robin fashion, skipping any stalled threads
When switch?
  Fine grain: alternate instruction per thread
    CPU must be able to switch threads every clock
  Coarse grain: when a thread is stalled, another thread can be executed
    Switches threads only on costly stalls, such as L2 cache misses
    The thread start time << stall time

## Slide 7: Fine-Grained Multithreading
Advantage
  It can hide both short and long stalls, since instructions from other threads executed when one thread stalls
Disadvantage
  It slows down execution of individual threads, since a thread ready to execute without stalls will be delayed by instructions from other threads

## Slide 8: Course-Grained Multithreading
Advantages
  Relieves need to have very fast thread-switching
  Doesn’t slow down thread, since instructions from other threads issued only when the thread encounters a costly stall
Disadvantages
  It is hard to overcome throughput losses from shorter stalls, due to a thread start-up costs
  Since CPU issues instructions from 1 thread, when a stall occurs, the pipeline must be emptied or frozen
  New thread must fill pipeline before instructions can complete

## Slide 9: Superscalar: Most Execution Units Lie Idle
For most apps, most execution units lie idle: an 8-way superscalar
From: Tullsen, Eggers, and Levy, Simultaneous Multithreading: Maximizing On-chip Parallelism, ISCA 1995.

## Slide 10: Simultaneous Multithreading (SMT)
SMT: dynamically scheduled already has HW to support multithreading
  Large set of virtual registers to hold the register sets of independent threads
  Register renaming provides unique register identifiers, so multiple threads instructions can be mixed in datapath without confusing
  Out-of-order completion allows out-of-order execution, and gets better HW utilization
Just adding a per thread RAT and keeping separate PCs and ROBs for each thread

## Slide 11: Processors and SMT Technology
Processors without SMT | 
Architecture States | 
Processor Execution Resources | 
Processor Interface | 
Processors with SMT | 
Architecture States | Architecture States
Processor Execution Resources | 
Processor Interface | 

## Slide 12: Simultaneous Multi-Threading (SMT) Execution
One thread, 8 units |  |  |  |  |  |  |  | 
CYCLE | M | M | FX | FX | FP | FP | BR | CC
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  | 
Two threads, 8 units |  |  |  |  |  |  |  | 
CYCLE | M | M | FX | FX | FP | FP | BR | CC
1 |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  | 
M = Load/Store, FX = Fixed Point, FP = Floating Point, BR = Branch, CC = Condition Codes

## Slide 13: Multithreaded Categories
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 14: Simple Multithreaded Pipeline
Have to carry thread select down pipeline to ensure correct state bits read/written at each pipe stage
Appears to software (including OS) as multiple, albeit slower, CPUs
+1
2
Thread select
PC
1
PC
1
PC
1
PC
1
I$
IR
GPR1
GPR1
GPR1
GPR1
X
Y
2
D$

## Slide 15: For most apps, most execution units lie idle in an OoO superscalar
From: Tullsen, Eggers, and Levy,
“Simultaneous Multithreading: Maximizing On-chip Parallelism”, ISCA 1995.
For an 8-way superscalar.

## Slide 16: Superscalar Machine Efficiency
Issue width
Time
Completely idle cycle (vertical waste)
Instruction issue
Partially filled cycle, i.e., IPC < 4
(horizontal waste)
Notes: Focus is switching to function unit efficiency (as a measure of throughput).

## Slide 17: Vertical Multithreading
Cycle-by-cycle interleaving removes vertical waste, but leaves some horizontal waste
Issue width
Time
Second thread interleaved cycle-by-cycle
Instruction issue
Partially filled cycle, i.e., IPC < 4
(horizontal waste)

## Slide 18: Chip Multiprocessing (CMP)
What is the effect of splitting into multiple processors?
  reduces horizontal waste,
  leaves some vertical waste, and
  puts upper limit on peak throughput of each thread.
Issue width
Time

## Slide 19: Ideal Superscalar Multithreading [Tullsen, Eggers, Levy, UW, 1995]
Interleave multiple threads to multiple issue slots with no restrictions
Issue width
Time

## Slide 20: O-o-O Simultaneous Multithreading [Tullsen, Eggers, Emer, Levy, Stamm, Lo, DEC/UW, 1996]
Add multiple contexts and fetch engines and allow instructions fetched from different threads to issue simultaneously
Utilize wide out-of-order superscalar processor issue queue to find instructions to issue from multiple threads
OOO instruction window already has most of the circuitry required to schedule from multiple threads
Any single thread can utilize whole machine

## Slide 21: SMT adaptation to parallelism type
For regions with high thread-level parallelism (TLP) entire machine width is shared by all threads
For regions with low thread-level parallelism (TLP) entire machine width is available for instruction-level parallelism (ILP)
Issue width
Time
Issue width
Time
Notes: Amdahl’s law…

## Slide 22: Performance with SMT
SMT makes sense only with fine-grained implementation
  Impact of fine-grained scheduling on single thread performance?
  A preferred thread approach sacrifices neither throughput nor single-thread performance?
  Unfortunately, with a preferred thread, the processor is likely to sacrifice some throughput, when preferred thread stalls

## Slide 23: Design Challenges in SMT
Larger register files needed to hold multiple contexts
Clock cycle time, especially in
  Instruction issue - more candidate instructions need to be considered
  Instruction completion - choosing which instructions to commit may be challenging
Ensuring that cache and TLB conflicts generated by SMT do not degrade performance

## Slide 24: Sun T1 and Intel i7
Effectiveness of Fine-Grained Multithreading on the Sun T1
  T1 Multithreading Unicore Performance
Effectiveness of Simultaneous Multithreading on Superscalar Processors
  The Intel i7 supports SMT with two threads

## Slide 25: Power 4
Single-threaded predecessor
8 execution units in out-of-order engine, each may issue an instruction each cycle

## Slide 26: Power 4 and 2-threaded Power 5
2 commits (architected register sets)
2 fetch (PC), 2 initial decodes

## Slide 27: Power 5 data flow ...
Why only 2 threads? With 4, one of the shared resources (physical registers, cache, memory bandwidth) would be prone to bottleneck

## Slide 28: Power 5 Thread Performance ...
Relative priority of each thread controllable in hardware
For balanced operation, both threads run slower than if they “owned” the machine

## Slide 29: Changes in Power 5 to Support SMT
The Power5 core is about 24% larger than the Power4 core because of the addition of SMT support
  Increased associatively of L1 I-cache and the instruction address translation buffers
  Added per thread load and store queues
  Increased size of the L2 (1.92 vs. 1.44 MB) and L3 caches
  Added separate instruction prefetch and buffering per thread
  Increased the virtual registers from 152 to 240
  Increased the size of several issue queues

## Slide 30: Performance Gains of Power5
Power 5, 8 processor server
  1.23 faster for SPECint_rate with SMT
  1.16 faster for SPECfp_rate
Power 5 running 2 copies of each app speedup between 0.89 and 1.41
  Most gained some
  FP apps had most cache conflicts and least gains

## Slide 31: Intel’s Hyper-Threading (HT) Technology
Intel’s hyper-threading (HT) technology brings the concept of simultaneous multi-threading (SMT) to the Intel architecture
HT technology makes a single physical processor appear as two processors
  The physical execution resources are shared and the architecture state is duplicated for the two logical processors
Intel’s HT is first implemented on the Intel Xeon processor

## Slide 32: Intel® Xeon™ Processor Pipeline

## Slide 33: Out-of-order Execution Engine Detailed Pipeline

## Slide 34: Single-task and Multi-task Modes

## Slide 35: Performance on an OLTP workload

## Slide 36: Web Server Benchmark Performance

## Slide 37: Performance of HT
Pentium 4 HT is a dual threaded SMT
Speedup
  1.01 for SPECint_rate
  1.07 for SPECfp_rate
Running on Pentium 4 each of 26 SPEC benchmarks paired with every other
  Speed-ups from 0.90 to 1.58
  Average was 1.20

## Slide 38: Head to Head ILP Competition
Processor | Micro architecture | Fetch / Issue / Execute | FU | Clock Rate (GHz) | Transis-tors Die size | Power
Intel Pentium 4 Extreme | Speculative dynamically scheduled; deeply pipelined; SMT | 3/3/4 | 7 int. 1 FP | 3.8 | 125 M 122 mm2 | 115 W
AMD Athlon 64 FX-57 | Speculative dynamically scheduled | 3/3/4 | 6 int. 3 FP | 2.8 | 114 M 115 mm2 | 104 W
IBM Power5 (1 CPU only) | Speculative dynamically scheduled; SMT; 2 CPU cores/chip | 8/4/8 | 6 int. 2 FP | 1.9 | 200 M 300 mm2 (est.) | 80W (est.)
Intel Itanium 2 | Statically scheduled VLIW-style | 6/5/11 | 9 int. 2 FP | 1.6 | 592 M 423 mm2 | 130 W

## Slide 39: Performance on SPECint2000

## Slide 40: Performance on SPECfp2000

## Slide 41: Normalized Performance: Efficiency
Rank | I tanium2 | Pen t I um4 | A t h l on64 | Powe r 5
Int/Trans | 4 | 2 | 1 | 3
FP/Trans | 4 | 2 | 1 | 3
Int/area | 4 | 2 | 1 | 3
FP/area | 4 | 2 | 1 | 3
Int/Watt | 4 | 3 | 1 | 2
FP/Watt | 2 | 4 | 3 | 1

## Slide 42: No Obvious Over All Leader in Performance
The Athlon leads on SPECInt
  Then Pentium4, Itanium2, and Power5
Athlon and Pentium 4 both make good use of transistors and area
IBM Power5 is the most effective user of energy on SPECFP
  Essentially tied on SPECINT
Itanium 2 is the most inefficient processor both for FP and integer code
  But one efficiency measure (SPECFP/Watt)

## Slide 43: Limits to ILP: Microarchitecture
Doubling issue rates above today’s 3-6 instructions per clock, say to 6 to 12 instructions, probably requires a processor to
  issue 3 or 4 data memory accesses per cycle,
  resolve 2 or 3 branches per cycle,
  rename and access more than 20 registers per cycle, and
  fetch 12 to 24 instructions per cycle

## Slide 44: Limits to ILP: Complexities
The complexities of implementing these capabilities is likely to mean sacrifices in the maximum clock rate
  E.g, widest issue processor is the Itanium 2, but it also has the slowest clock rate, despite the fact that it consumes the most power!

## Slide 45: Limits to ILP: Energy Efficient
Most techniques for increasing performance increase power consumption
The key question is whether a technique is energy efficient:
  Does it increase power consumption faster than it increases performance?
  Multiple issue processors techniques all are energy inefficient:
    Issuing multiple instructions incurs some overhead in logic that grows faster than the issue rate grows

## Slide 46: ILP or TLP
Right balance of ILP and TLP is unclear today
Perhaps right choice
  For server market, which can exploit more TLP
  May differ from desktop, where single-thread performance may continue to be a primary requirement (ILP)

## Slide 47: Homework
Review
  3.12, 3.13
Papers
  Tullsen, Eggers, and Levy, “Simultaneous Multithreading: Maximizing On-chip Parallelism”, ISCA 1995
  IBM Power8的单线程性能为何如此孱弱？

## Slide 48: Next...
Professor Wang

## Slide 49: Thank u 4 your attention!
CU in final examination 